## Slide 1: Control Systems (CS)
Dr. Imtiaz Hussain
Associate Professor
Mehran University of Engineering & Technology Jamshoro, Pakistan
email: imtiaz.hussain@faculty.muet.edu.pk
URL :http://imtiazhussainkalwar.weebly.com/
Lecture-6-7
Mathematical Modeling of Electromechanical Systems

## Slide 2: Electromechanical Systems
Electromechanics combines electrical and mechanical processes.
Devices which carry out electrical operations by using moving parts are known as electromechanical.
  Relays
  Solenoids
  Electric Motors
  Electric Generators
  Switches and e.t.c

## Slide 3: Example-1: Potentiometer

## Slide 4: Example-1: Potentiometer
The resistance between the wiper (slider) and "A" is labeled R1, the resistance between the wiper and "B" is labeled R2.
The total resistance between "A" and "B" is constant, R1+R2=Rtot.
If the potentiometer is turned to the extreme counterclockwise position such that the wiper is touching "A" we will call this θ=0; in this position R1=0 and R2=Rtot.
If the wiper is in the extreme clockwise position such that it is touching "B" we will call this θ=θmax; in this position R1=Rtot and R2=0.

## Slide 5: Example-1: Potentiometer
R1 and R2 vary linearly with θ between the two extremes:

## Slide 6: Example-1: Potentiometer
Potentiometer can be used to sense angular position, consider the circuit of figure-1.
Using the voltage divider principle we can write:
Figure-1

## Slide 7
D.C Drives
Speed control can be achieved using DC drives in a number of ways.
Variable Voltage can be applied to the armature terminals of the DC motor .
Another method is to vary the flux per pole of the motor.
The first method involve adjusting the motor’s armature while the latter method involves adjusting the motor field. These methods are referred to as “armature control” and “field control.”

## Slide 8
D.C Drives
Motor Characteristics
For every motor, there is a specific Torque/Speed curve and Power curve.
Torque is inversely proportional to the speed of the output shaft.
Motor characteristics are frequently given as two points on this graph:
The stall torque,, represents the point on the graph at which the torque is maximum, but the shaft is not rotating.
The no load speed is the maximum output speed of the motor.

## Slide 9
D.C Drives
Motor Characteristics
Power is defined as the product of torque and angular velocity.

## Slide 10
Mechanical Subsystem
Input: voltage u
Output: Angular velocity 
Elecrical Subsystem (loop method):
Example-2: Armature Controlled D.C Motor
u
ia
T
Ra
La
J

B
eb
Vf=constant

## Slide 11
Torque-Current:
Voltage-Speed:
Combing previous equations results in the following mathematical model:
Power Transformation:
where Kt: torque constant, Kb: velocity constant For an ideal motor
Example-2: Armature Controlled D.C Motor
u
ia
T
Ra
La
J

B
eb
Vf=constant

## Slide 12
Taking Laplace transform of the system’s differential equations with zero initial conditions gives:
Eliminating Ia yields the input-output transfer function
Example-2: Armature Controlled D.C Motor

## Slide 13: Reduced Order Model
Assuming small inductance, La 0
which is equivalent to

B
The D.C. motor provides an input torque and an additional damping effect known as back-emf damping
Example-2: Armature Controlled D.C Motor

## Slide 14
If output of the D.C motor is angular position θ then we know
Which yields following transfer function
Example-2: Armature Controlled D.C Motor
u
ia
T
Ra
La
J
θ
B
eb
Vf=constant

## Slide 15
Applying KVL at field circuit
Example-3: Field Controlled D.C Motor
if
Tm
Rf
Lf
J
ω
B
Ra
La
ea
ef
Mechanical Subsystem

## Slide 16
Torque-Current:
Combing previous equations and taking Laplace transform (considering initial conditions to zero) results in the following mathematical model:
Power Transformation:
where Kf: torque constant
Example-3: Field Controlled D.C Motor

## Slide 17
If angular position θ is output of the motor
Eliminating If(S) yields
Example-3: Field Controlled D.C Motor
if
Tm
Rf
Lf
J
θ
B
Ra
La
ea
ef

## Slide 18
An armature controlled D.C motor runs at 5000 rpm when 15v applied at the armature circuit. Armature resistance of the motor is 0.2 Ω, armature inductance is negligible, back emf constant is 5.5x10-2 v sec/rad, motor torque constant is 6x10-5, moment of inertia of motor 10-5, viscous friction coeffcient is negligible, moment of inertia of load is 4.4x10-3, viscous friction coeffcient of load is 4x10-2.
Drive the overall transfer function of the system i.e. ΩL(s)/ Ea(s)
Determine the gear ratio such that the rotational speed of the load is reduced to half and torque is doubled.
Example-4
15 v
ia
T
Ra
La
Jm

Bm
eb
Vf=constant
JL
N1
N2
BL
L
ea

## Slide 19
System constants
ea = armature voltage
eb = back emf
Ra = armature winding resistance = 0.2 Ω
La = armature winding inductance = negligible
ia = armature winding current
Kb = back emf constant = 5.5x10-2 volt-sec/rad
Kt = motor torque constant = 6x10-5 N-m/ampere
Jm = moment of inertia of the motor = 1x10-5 kg-m2
Bm=viscous-friction coefficients of the motor = negligible
JL = moment of inertia of the load = 4.4x10-3 kgm2
BL = viscous friction coefficient of the load = 4x10-2 N-m/rad/sec
gear ratio = N1/N2

## Slide 20
Since armature inductance is negligible therefore reduced order transfer function of the motor is used.
Example-4
15 v
ia
T
Ra
La
Jm

Bm
eb
Vf=constant
JL
N1
N2
BL
L
ea

## Slide 21
A field controlled D.C motor runs at 10000 rpm when 15v applied at the field circuit. Filed resistance of the motor is 0.25 Ω, Filed inductance is 0.1 H, motor torque constant is 1x10-4, moment of inertia of motor 10-5, viscous friction coefficient is 0.003, moment of inertia of load is 4.4x10-3, viscous friction coefficient of load is 4x10-2.
Drive the overall transfer function of the system i.e. ΩL(s)/ Ef(s)
Determine the gear ratio such that the rotational speed of the load is reduced to 500 rpm.
Example-5
if
Tm
Rf
Lf
Jm
ωm
Bm
Ra
La
ea
ef
JL
N1
N2
BL
L

## Slide 22
+
kp
-
JL
_
ia
eb
Ra
La
+
T
r
c
ea
_
+
e
_
+
N1
N2
BL
θ
if = Constant
JM BM
Example-6: Angular Position Control System

## Slide 23
Numerical Values for System constants
r = angular displacement of the reference input shaft
c = angular displacement of the output shaft
θ = angular displacement of the motor shaft
K1 = gain of the potentiometer shaft = 24/π
Kp = amplifier gain = 10
ea = armature voltage
eb = back emf
Ra = armature winding resistance = 0.2 Ω
La = armature winding inductance = negligible
ia = armature winding current
Kb = back emf constant = 5.5x10-2 volt-sec/rad
Kt = motor torque constant = 6x10-5 N-m/ampere
Jm = moment of inertia of the motor = 1x10-5 kg-m2
Bm=viscous-friction coefficients of the motor = negligible
JL = moment of inertia of the load = 4.4x10-3 kgm2
BL = viscous friction coefficient of the load = 4x10-2 N-m/rad/sec
n= gear ratio = N1/N2 = 1/10

## Slide 24
Example-6: Angular Position Control System
Transfer function of the armature controlled D.C motor with load connected to it is given by
Where

## Slide 25
Example-6: Angular Position Control System
Error is difference between reference input and out calculated and can be calculated as
Output of amplifier is
Merging eq (a) and eq (b) yields
Relation between angular position of motor and angular position of load is given as
or
E
(a)
(b)

## Slide 26
Example-6: Angular Position Control System
Final Closed loop transfer function of the system can now be written as

## Slide 27: End of Lectures-6-7
To download this lecture visit
http://imtiazhussainkalwar.weebly.com/