## Slide 1: Modern Control Systems (MCS)
Dr. Imtiaz Hussain
email: imtiaz.hussain@faculty.muet.edu.pk
URL :http://imtiazhussainkalwar.weebly.com/
Lecture-16-17
Design of Control Systems in Sate Space

## Slide 2: Lecture Outline
Introduction
Pole Placement
  Topology of Pole Placement
  Pole Placement Design Techniques
    Using Transformation Matrix P
    Direct Substitution Method
    Ackermann’s Formula

## Slide 3: Introduction
One of the drawbacks of frequency domain methods of design is that after designing the location of the dominant second-order pair of poles, we keep our fingers crossed, hoping that the higher-order poles do not affect the second-order approximation.
What we would like to be able to do is specify all closed-loop poles of the higher-order system.

## Slide 4: Introduction
Frequency domain methods of design do not allow us to specify all poles in systems of order higher than 2 because they do not allow for a sufficient number of unknown parameters to place all of the closed-loop poles uniquely.
One gain to adjust, or compensator pole and zero to select, does not yield a sufficient number of parameters to place all the closed-loop poles at desired locations.

## Slide 5: Introduction
Remember, to place n unknown quantities, you need n adjustable parameters.
State-space methods solve this problem by introducing into the system
  Other adjustable parameters and
  The technique for finding these parameter values
On the other hand, state-space methods do not allow the specification of closed-loop zero locations, which frequency domain methods do allow through placement of the lead compensator zero.

## Slide 6: Introduction
Finally, there is a wide range of computational support for state-space methods; many software packages support the matrix algebra required by the design process.
However, as mentioned before, the advantages of computer support are balanced by the loss of graphic insight into a design problem that the frequency domain methods yield.

## Slide 7: Pole Placement
In this lecture we will discuss a design method commonly called the pole-placement or pole-assignment technique.
We assume that all state variables are measurable and are available for feedback.
If the system considered is completely state controllable, then poles of the closed-loop system may be placed at any desired locations by means of state feedback through an appropriate state feedback gain matrix.

## Slide 8: Pole Placement
The present design technique begins with a determination of the desired closed-loop poles based on the transient-response and/or frequency-response requirements, such as speed, damping ratio, or bandwidth, as well as steady-state requirements.
By choosing an appropriate gain matrix for state feedback, it is possible to force the system to have closed-loop poles at the desired locations, provided that the original system is completely state controllable.

## Slide 9: Topology of Pole Placement
Consider a plant represented in state space by

## Slide 10: Topology of Pole Placement
In a typical feedback control system, the output, y, is fed back to the summing junction.
It is now that the topology of the design changes. Instead of feeding back y, we feed back all of the state variables.
If each state variable is fed back to the control, u, through a gain, ki, there would be n gains, ki, that could be adjusted to yield the required closed-loop pole values.

## Slide 11: Topology of Pole Placement
The feedback through the gains, ki, is represented in following figure by the feedback vector K.

## Slide 12: Topology of Pole Placement
For example consider a plant signal-flow graph in phase-variable form

## Slide 13: Topology of Pole Placement
Each state variable is then fed back to the plant’s input, u, through a gain, ki, as shown in Figure

## Slide 14: Pole Placement
We will limit our discussions to single-input, single-output systems (i.e. we will assume that the control signal u(t) and output signal y(t) to be scalars).
We will also assume that the reference input r(t) is zero.

## Slide 15: Pole Placement
The stability and transient response characteristics are determined by the eigenvalues of matrix A-BK.
If matrix K is chosen properly Eigenvalues of the system can be placed at desired location.
And the problem of placing the regulator poles (closed-loop poles) at the desired location is called a pole-placement problem.

## Slide 16: Pole Placement
  There are three approaches that can be used to determine the gain matrix K to place the poles at desired location.
    Using Transformation Matrix P
    Direct Substitution Method
    Ackermann’s formula
  All those methods yield the same result.

## Slide 17: Pole Placement (Using Transformation Matrix P)
  Following are the steps to be followed in this particular method.
  Check the state controllability of the system

## Slide 18: Pole Placement (Using Transformation Matrix P)
  Following are the steps to be followed in this particular method.
  Transform the given system in CCF.
s+

## Slide 19: Pole Placement (Using Transformation Matrix P)
  Following are the steps to be followed in this particular method.
  Obtain the desired characteristic equation from desired Eigenvalues.
    If the desired Eigenvalues are , , ,

## Slide 20: Pole Placement (Using Transformation Matrix P)
  Following are the steps to be followed in this particular method.
  Compute the gain matrix K.

## Slide 21: Pole Placement (Using Transformation Matrix P)
  Example-1: Consider the regulator system shown in following figure. The plant is given by
  The system uses the state feedback control u=-Kx. The desired eigenvalues are , ,. Determine the state feedback gain matrix K.

## Slide 22: Pole Placement (Using Transformation Matrix P)
  Example-1: Step-1
First, we need to check the controllability matrix of the system. Since the controllability matrix CM is given by
We find that rank(CM)=3. Thus, the system is completely state controllable and arbitrary pole placement is possible.

## Slide 23: Pole Placement (Using Transformation Matrix P)
  Example-1: Step-2 (Transformation to CCF)
The given system is already in CCF

## Slide 24: Pole Placement (Using Transformation Matrix P)
  Example-1: Step-3
Determine the characteristic equation
Hence

## Slide 25: Pole Placement (Using Transformation Matrix P)
  Example-1: Step-4
The desired characteristics polynomial can be computed using desired eigenvalues
Hence

## Slide 26: Pole Placement (Using Transformation Matrix P)
  Example-1: Step-4
State feedback gain matric K is then calculated as

## Slide 27: Pole Placement (Using Transformation Matrix P)
∫
∫
∫
-6
-5
-5
State diagram of the given system

## Slide 28
∫
∫
∫
-6
-5
-5
199
55
8
-1

## Slide 29: Pole Placement (Direct Substitution Method)
  Following are the steps to be followed in this particular method.
  Check the state controllability of the system

## Slide 30: Pole Placement (Direct Substitution Method)
  Following are the steps to be followed in this particular method.
  Define the state feedback gain matrix as
  And equating with desired characteristic equation.

## Slide 31: Pole Placement (Using Direct Substitution)
  Example-1: Consider the regulator system shown in following figure. The plant is given by
  The system uses the state feedback control u=-Kx. The desired eigenvalues are , ,. Determine the state feedback gain matrix K.

## Slide 32: Pole Placement (Using Transformation Matrix P)
  Example-1: Step-1
First, we need to check the controllability matrix of the system. Since the controllability matrix CM is given by
We find that rank(CM)=3. Thus, the system is completely state controllable and arbitrary pole placement is possible.

## Slide 33: Pole Placement (Using Transformation Matrix P)
  Example-1: Step-2
  Let K be
Desired characteristic polynomial is obtained as
Comparing the coefficients of powers of s
5

## Slide 34: Pole Placement (Ackermann’s Formula)
  Following are the steps to be followed in this particular method.
  Check the state controllability of the system

## Slide 35: Pole Placement (Ackermann’s Formula)
  Following are the steps to be followed in this particular method.
  Use Ackermann’s formula to calculate K

## Slide 36: Pole Placement (Ackermann’s Formula)
  Example-1: Consider the regulator system shown in following figure. The plant is given by
  The system uses the state feedback control u=-Kx. The desired eigenvalues are , ,. Determine the state feedback gain matrix K.

## Slide 37: Pole Placement (Using Transformation Matrix P)
  Example-1: Step-1
First, we need to check the controllability matrix of the system. Since the controllability matrix CM is given by
We find that rank(CM)=3. Thus, the system is completely state controllable and arbitrary pole placement is possible.

## Slide 38: Pole Placement (Ackermann’s Formula)
  Following are the steps to be followed in this particular method.
  Use Ackermann’s formula to calculate K
  are the coefficients of the desired characteristic polynomial.

## Slide 39: Pole Placement (Ackermann’s Formula)

## Slide 40: Pole Placement (Ackermann’s Formula)

## Slide 41: Pole Placement
  Example-2: Consider the regulator system shown in following figure. The plant is given by
  Determine the state feedback gain for each state variable to place the poles at -1+j, -1-j,-3. (Apply all methods)

## Slide 42: End of Lectures-16-17
To download this lecture visit
http://imtiazhussainkalwar.weebly.com/