## Slide 1: Control Systems (CS)
Dr. Imtiaz Hussain
Associate Professor
Mehran University of Engineering & Technology Jamshoro, Pakistan
email: imtiaz.hussain@faculty.muet.edu.pk
URL :http://imtiazhussainkalwar.weebly.com/
Lecture-4
Signal Flow Graph Representation of Control Systems
Note: I do not claim any originality in these lectures. The contents of this presentation are mostly taken from the book of Ogatta, Norman Nise, Bishop and B C. Kuo and various other internet sources.
6th Semester 14ES (SEC-I)

## Slide 2: Outline
Introduction to Signal Flow Graphs
  Definitions
  Terminologies
  Examples
Mason’s Gain Formula
  Examples
Signal Flow Graph from Block Diagrams
Design Examples

## Slide 3: Introduction
Alternative method to block diagram representation, developed by Samuel Jefferson Mason.
Advantage: the availability of a flow graph gain formula, also called Mason’s gain formula.
A signal-flow graph consists of a network in which nodes are connected by directed branches.
It depicts the flow of signals from one point of a system to another and gives the relationships among the signals.

## Slide 4: Fundamentals of Signal Flow Graphs
Consider a simple equation below and draw its signal flow graph:
The signal flow graph of the equation is shown below;
Every variable in a signal flow graph is represented by a Node.
Every transmission function in a signal flow graph is represented by a Branch.
Branches are always unidirectional.
The arrow in the branch denotes the direction of the signal flow.

## Slide 5
Signal-Flow Graph Models

## Slide 6
Signal-Flow Graph Models
r1 and r2 are inputs and x1 and x2 are outputs

## Slide 7: Signal-Flow Graph Models
b
x4
x3
x2
x1
x0
h
f
g
e
d
c
a
xo is input and x4 is output

## Slide 8: Terminologies
An input node or source contain only the outgoing branches. i.e., X1
An output node or sink contain only the incoming branches. i.e., X4
A path is a continuous, unidirectional succession of branches along which no node is passed more than ones. i.e.,
A forward path is a path from the input node to the output node. i.e.,
X1 to X2 to X3 to X4 , and X1 to X2 to X4 , are forward paths.
A feedback path or feedback loop is a path which originates and terminates on the same node. i.e.; X2 to X3 and back to X2 is a feedback path.
X1 to X2 to X3 to X4
X1 to X2 to X4
X2 to X3 to X4

## Slide 9: Terminologies
A self-loop is a feedback loop consisting of a single branch. i.e.; A33 is a self loop.
The gain of a branch is the transmission function of that branch.
The path gain is the product of branch gains encountered in traversing a path. i.e. the gain of forwards path X1 to X2 to X3 to X4 is A21A32A43
The loop gain is the product of the branch gains of the loop. i.e., the loop gain of the feedback loop from X2 to X3 and back to X2 is A32A23.
Two loops, paths, or loop and a path are said to be non-touching if they have no nodes in common.

## Slide 10: Consider the signal flow graph below and identify the following
Input node.
Output node.
Forward paths.
Feedback paths (loops).
Determine the loop gains of the feedback loops.
Determine the path gains of the forward paths.
Non-touching loops

## Slide 11: Consider the signal flow graph below and identify the following
There are two forward path gains;

## Slide 12: Consider the signal flow graph below and identify the following
There are four loops

## Slide 13: Consider the signal flow graph below and identify the following
Nontouching loop gains;

## Slide 14: Consider the signal flow graph below and identify the following
Input node.
Output node.
Forward paths.
Feedback paths.
Self loop.
Determine the loop gains of the feedback loops.
Determine the path gains of the forward paths.

## Slide 15: Input and output Nodes
Input node
Output node

## Slide 16: (c) Forward Paths

## Slide 17: (d) Feedback Paths or Loops

## Slide 18: (d) Feedback Paths or Loops

## Slide 19: (d) Feedback Paths or Loops

## Slide 20: (d) Feedback Paths or Loops

## Slide 21: (e) Self Loop(s)

## Slide 22: (f) Loop Gains of the Feedback Loops

## Slide 23: (g) Path Gains of the Forward Paths

## Slide 24: Mason’s Rule (Mason, 1953)
The block diagram reduction technique requires successive application of fundamental relationships in order to arrive at the system transfer function.
On the other hand, Mason’s rule for reducing a signal-flow graph to a single transfer function requires the application of one formula.
The formula was derived by S. J. Mason when he related the signal-flow graph to the simultaneous equations that can be written from the graph.

## Slide 25: Mason’s Rule:
The transfer function, C(s)/R(s), of a system represented by a signal-flow graph is;
Where
n = number of forward paths.
Pi = the i th forward-path gain.
∆ = Determinant of the system
∆i = Determinant of the ith forward path
∆ is called the signal flow graph determinant or characteristic function. Since ∆=0 is the system characteristic equation.

## Slide 26: Mason’s Rule:
∆ = 1- (sum of all individual loop gains) + (sum of the products of the gains of all possible two loops that do not touch each other) – (sum of the products of the gains of all possible three loops that do not touch each other) + … and so forth with sums of higher number of non-touching loop gains
∆i = value of Δ for the part of the block diagram that does not touch the i-th forward path (Δi = 1 if there are no non-touching loops to the i-th path.)

## Slide 27
Systematic approach
Calculate forward path gain Pi for each forward path i.
Calculate all loop transfer functions
Consider non-touching loops 2 at a time
Consider non-touching loops 3 at a time
etc
Calculate Δ from steps 2,3,4 and 5
Calculate Δi as portion of Δ not touching forward path i

## Slide 28: Example#1: Apply Mason’s Rule to calculate the transfer function of the system represented by following Signal Flow Graph
Therefore,
There are three feedback loops

## Slide 29: Example#1: Apply Mason’s Rule to calculate the transfer function of the system represented by following Signal Flow Graph
∆ = 1- (sum of all individual loop gains)
There are no non-touching loops, therefore

## Slide 30: Example#1: Apply Mason’s Rule to calculate the transfer function of the system represented by following Signal Flow Graph
∆1 = 1- (sum of all individual loop gains)+...
Eliminate forward path-1
∆1 = 1
∆2 = 1- (sum of all individual loop gains)+...
Eliminate forward path-2
∆2 = 1

## Slide 31: Example#1: Continue

## Slide 32: Example#2: Apply Mason’s Rule to calculate the transfer function of the system represented by following Signal Flow Graph
2. Calculate all loop gains.
3. Consider two non-touching loops.
L1L3 L1L4
L2L4 L2L3
1. Calculate forward path gains for each forward path.
P1
P2

## Slide 33: Example#2: continue
Consider three non-touching loops.
None.
Calculate Δ from steps 2,3,4.

## Slide 34
Example#2: continue
Eliminate forward path-1
Eliminate forward path-2

## Slide 35
Example#2: continue

## Slide 36: Example#3
Find the transfer function, C(s)/R(s), for the signal-flow graph in figure below.

## Slide 37: Example#3
There is only one forward Path.

## Slide 38: Example#3
There are four feedback loops.

## Slide 39: Example#3
Non-touching loops taken two at a time.

## Slide 40: Example#3
Non-touching loops taken three at a time.

## Slide 41: Example#3
Eliminate forward path-1

## Slide 42: Example#4: Apply Mason’s Rule to calculate the transfer function of the system represented by following Signal Flow Graph
There are three forward paths, therefore n=3.

## Slide 43: Example#4: Forward Paths

## Slide 44: Example#4: Loop Gains of the Feedback Loops

## Slide 45: Example#4: two non-touching loops

## Slide 46: Example#4: Three non-touching loops

## Slide 47: From Block Diagram to Signal-Flow Graph Models Example#5
G1
G4
G3
－
－
－
C(s)
R(s)
G1
G2
H2
H1
G4
G3
H3
E(s)
X1
X2
X3
R(s)
C(s)
－H2
－H1
－H3
X1
X2
X3
E(s)
1
G2

## Slide 48: From Block Diagram to Signal-Flow Graph Models Example#5
R(s)
－H2
1
G4
G3
G2
G1
1
C(s)
－H1
－H3
X1
X2
X3
E(s)

## Slide 49: Example#6
G1
G2
+
－
+
－
－
－
+
C(s)
R(s)
E(s)
Y2
Y1
X1
X2
－
1
-1
1
-1
-1
-1
-1
1
1
G1
G2
1
R(s)
E(s)
C(s)
X1
X2
Y2
Y1

## Slide 50: Example#6
1
-1
1
-1
-1
-1
-1
1
1
G1
G2
1
R(s)
E(s)
C(s)
X1
X2
Y2
Y1
7 loops:
3 ‘2 non-touching loops’ :

## Slide 51: Example#6
1
-1
1
-1
-1
-1
-1
1
1
G1
G2
1
R(s)
E(s)
C(s)
X1
X2
Y2
Y1
Then:
4 forward paths:

## Slide 52: Example#6
We have

## Slide 53: Example-7: Determine the transfer function C/R for the block diagram below by signal flow graph techniques.
The signal flow graph of the above block diagram is shown below.
There are two forward paths. The path gains are
The three feedback loop gains are
No loops are non-touching, hence
Since no loops touch the nodes of P2, therefore
Because the loops touch the nodes of P1, hence
Hence the control ratio T = C/R is

## Slide 54: Example-6: Find the control ratio C/R for the system given below.
The two forward path gains are
The signal flow graph is shown in the figure.
The five feedback loop gains are
Hence the control ratio T =
There are no non-touching loops, hence
All feedback loops touches the two forward paths, hence

## Slide 55: Design Example#1

## Slide 56: Design Example#2

## Slide 57: Design Example#2

## Slide 58: Design Example#2

## Slide 59: End of Lecture-4
To download this lecture visit
http://imtiazhussainkalwar.weebly.com/