## Slide 1: FPGA Based System Design
Dr. Tayab Din Memon
tayabuddin.memon@faculty.muet.edu.pk
Lecture 20 & 21

## Slide 2: Intro to Test Benches
The simulation of a design refers to the role of the model within the design process; specifically:
  exploring design alternatives,
  testing functional requirements satisfaction/correctness
  early removal of design errors through simulation, correction, and regression testing
  early verification of software at the block functional level and at more detailed levels
Notes: Now analyse the behaviour of the code. If sel is '1', f gets a. But what happens when sel is '0'? Well, very simply, nothing! f does not and can not change. When sel is fixed at '0', we can change a as much as we like, f will not be assigned the value of a. If we suppose that an if statement synthesises to a multiplexer, then we must be able to configure the multiplexer such that f only gets the value of a when sel is '1'. This can be achieved by feeding back the multiplexer f output back to the '0' input. in hardware terms this is a transparent latch and this is exactly the hardware synthesized by a synthesis tool given this VHDL code.

## Slide 3: Test Bench
Test Bench
ShiftComp
Shift
Comp
Test bench becomes top level of design
  can be larger and more complex than actual design
  use structural level of abstraction to connect lower level design descriptions

## Slide 4: Test Benches
Provide stimulus for simulation
  Functional descriptions used to generate input
Apply stimulus to the entity under test
  Locally declared signals connected to ports of components in the system
Compare output responses with expected values
  Functional descriptions used to compare model outputs to expected responses, alerts are raised when the model returns an unexpected result
Notes: The test bench is a self-contained top level component in the system hierarchy. It does not have any I/O pins (i.e. there are no PORT signals in its entity declaration)
In addition to instantiating the necessary components necessary to describe the system, a test bench may contain a behavioral VHDL description which may be used to generate stimulus patterns to the system as well as expected results which can then be compared with the outputs of the system’s subcomponents.

## Slide 5: Test Bench
apply
stimulus
data Q
load
clk
rst
A
EQ
B
check
results
Unit under test
Test Bench
Virtual circuit tester
  Written using one or more sequential processes
  Signal assignments
  Wait statements
  Repetitive stimulus
    eg. Clock
  assert statement
Notes: This slide, once again, highlights the use of test benches as a “virtual circuit tester”.
The test bench is akin to applying a test circuit to a device to verify its operation (hence the “virtual circuit tester” paradigm).

## Slide 6: Test Bench: example
library ieee; -- load the ieee 1164 library
use ieee.std_logic_1164.all; -- make the package “visible”
use work.nandgate; -- use NAND gate model from ‘work’
entity testnand is -- top level entity of the test bench
end testnand; -- has no ports
architecture stimulus of testnand is
component nand -- first declare lower level entity
port (A,B: in std_logic;
Y: out std_logic);
end component;
signal A,B: std_logic; -- next, declare some local signals to
signal Y: std_logic; -- assign values and observe
begin
-- create an instance of the comparator circuit.
NAND1: nandgate port map(A => A, B =>B, Y => Y);
entity decl.
for test bench
Unit under
test: includes
local signals
to apply stim
and measure
response
Component
instantiation

## Slide 7: Test Bench: example
-- now define a process to apply some stimulus over time
process
constant PERIOD: time := 40ns;
begin
A <= ‘1’;
B <= ‘1’;
wait for PERIOD;
assert (Y=‘0’)
report ‘Test failed’ severity ERROR;
A <= ‘1’;
B <= ‘0’;
wait for PERIOD;
assert (Y=‘1’)
report ‘Test failed’ severity ERROR;
A <= ‘0’;
B <= ‘1’;
wait for PERIOD;
assert (Y=‘1’)
report ‘Test failed’ severity ERROR;
A <= ‘0’;
B <= ‘0’;
wait for PERIOD;
assert (Y=‘1’)
report ‘Test failed’ severity ERROR;
wait;
end process;
end stimulus;
process
describes the
inputs to the
circuit over time
Wait: provides specific
delay value
assert condition_expression
report text_string
severity severity_level;
if condition_expression fails
then report string displayed
and simulator takes action depending
on severity.

## Slide 8: Cycle Testbench
For a cycle testbench, use processes with behavioral wait statements to create timing in the testbench and to model asynchronous activity.
Behavioral wait statements do not conform to the synthesis policy. For example, “wait for time” is a behavioral wait statement. Thus, these processes are identified as testbench processes (see above).

## Slide 9: Clock and Reset Generation for cycle TB

## Slide 11: Data Generation

## Slide 12: Assert Statement
ASSERT statements are used to print messages at the simulation console when specified runtime conditions are met
ASSERT statements defined one of four severity levels :
  Note -- relays information about conditions to the user
  Warning -- alerts the user to conditions that are not expected, but not fatal
  Error -- relays conditions that will cause the model to work incorrectly
  Failure -- alerts the user to conditions that are catastrophic
Notes: The Assert statement is used to alert the user of some condition occurring inside the model. When the condition in the Assert statement is False, the associated text message is displayed on the simulator console.
An evaluation of False may be used to halt the simulation, depending on the severity level of the associated Assert statement.
The four severity levels, in increasing severity, are listed in this slide. However, the simulator actions associated with each severity level are simulator dependent. For example, a simulator implementation may use the Failure condition to halt a simulation but continue a simulation under the other assertion conditions.

## Slide 13: Assert Statements
Syntax of the Assert statement
  assert condition report “violation statement” severity level;
When the specified condition is false, the Assert statement triggers and the report is issued
The violation statement is enclosed in quotes
  assert not((s=‘1’) and (r=‘1’)) report “Set and Reset are both 1” severity error;
Notes: This slide shows the syntax of the Assert statement. The Assert statement will trigger when the condition is false. The Report statement to be displayed is enclosed in quotes.
The Set and Reset lines of the S-R flip-flop in this example cannot simultaneously equal one. Therefore, the Assert statement evaluates to False (most easily described using the Not function) if this situation is observed during simulation.

## Slide 14: Assert Statements An Example
Assume good = ‘1’, reset = ‘0’
  procedure display_state (current_state : in state) is
  begin assert not(current_state = good) report “Status of State: good” severity note; assert not(current_state = reset) report “Status of State: reset” severity warning;
  end display_state;
Notes: The example shown here shows how the Assert statements are used to display the current state of an FSM. Note that these Assert statements are concurrent. Asserts can be concurrent or sequential depending on whether they appear outside or inside VHDL processes, respectively. Asserts can also be put in entity statements.

## Slide 15: Writing Test Vectors
File I/O Approach
  suitable for large vector arrays
  standard procedures for characters, strings and bits
procedure Readline(F:in Text; L:out Line);
procedure Writeline(F:out Text; L:in Line);
procedure Read(L:inout Line; Value:out std_logic; Good:out boolean);
procedure Read(L:inout Line; Value:out std_logic);
procedure Read(L:inout Line; Value:out std_logic_vector; Good:out boolean);
procedure Read(L:inout Line; Value:out std_logic_vector);
procedure Write(L:inout Line; Value:in std_logic; Justified:in Side := Right; Field:in Width :=0);
procedure Write(L:inout Line; Value:in std_logic_vector; Justified:in Side := Right; Field:in Width :=0);
Notes: One useful method of providing test vectors to a design is to implement a file-based approach. The test vectors would be stored in an external data file and the test bench itself simply reads each vector off the file and applies it to the component under test.
This approach lends itself useful for testing very complex designs, where it would be feasible to tinker with the test vectors separate from the test bench itself (this way, all that is needed is to re-run the simulation with the updated data file, as opposed to rewriting the test bench itself)

## Slide 16: Writing Test Vectors
Alternative approach
  create sequence of fixed input and expected output values
  multidimensional arrays/records
-- This constant declaration describes the test vectors to be applied to the design and expected result after a rising clock edge
constant test_vectors: test_array := (
-- CE, Set, Din, CRC_SUM (‘0’, ‘1’, ‘0’, ‘----------------’), -- reset (‘1’, ‘0’, ‘0’, ‘----------------’), -- ‘H’ (‘1’, ‘0’, ‘1’, ‘----------------’), (‘1’, ‘0’, ‘0’, ‘----------------’), (‘1’, ‘0’, ‘0’, ‘----------------’), (‘1’, ‘0’, ‘1’, ‘----------------’), (‘1’, ‘0’, ‘0’, ‘----------------’), (‘1’, ‘0’, ‘0’, ‘----------------’), (‘1’, ‘0’, ‘0’, ‘0010100000111100’), -- x283C etc...
stimulus
Expected response (don’t cares in this case)
Notes: The alternative approach to writing test vectors is to setup an array of vectors (be it through multidimensional arrays or arrays of records). Each vector contains the input stimulus, and its corresponding expected output. All that remains to be implemented is a test bench process that inputs the input stimuli to the component under test, read the components output, compare it to the expected output, and return feedback to the end result (usually through an assert statement)
This approach is useful, generally, for simple component designs (where there are few inputs and few possible outputs), and independently testing sub-components within a design.

## Slide 17: Creating Test Stimuli
Using loops and multiple processes
  can result in concise descriptions of complex input/output relationships
Clock1: process variable clktemp: std_logic := ‘1’;
begin while done /= true loop wait for PERIOD/2; clktemp := not clktemp; end loop; wait;
end process;
Multiple processes create clocks and input stimulus
Stimulus1: process
begin reset <= ‘1’; wait for PERIOD; reset <= ‘0’; mode <= ‘0’; wait for PERIOD; data <= (others => ‘1’); wait for PERIOD; mode <= ‘1’; for i in 0 to 127 loop wait for PERIOD; assert (VS = ‘1’) report “VS high at wrong place”; severity ERROR; end loop;
end process;
Notes: This test bench example shows how one would implement a test bench in VHDL where mutually exclusive input stimulus exists. In the case above, a clock process is used to generate a common clock signal (independent of any other process within the test bench). The other process tests an example component by providing stimulus to it.
This type of test bench approach is useful when testing multiple components within an overall design, or simultaneously testing functional units within the same component (sub-components, independent execution blocks, etc...)

## Slide 18: Automatic Test Benches
Timing diagram editors: timing  VHDL code
eg Waveformer®
  clocks & signals
  graphical waveform states (high, low, tri-state, valid, invalid, weak high, weak low)
  virtual busses with hex, binary, and other data values
  VHDL user-defined types and integer types
Notes: An alternate to implementing a full-scale test bench in VHDL is to utilise the in-built testing capabilities available in an EDA. Typically this is done by virtue of a timing editor (to allow the user to directly generate waveforms, suitable for testing a design).
The slide above highlights just how functional such in-built testing can be (with the ability to use a myriad of states, data types and signal types)

## Slide 19: End of the lecture
11 & 12 TEST BENCH