## Slide 1: Feedback Control Systems (FCS)
Dr. Imtiaz Hussain
email: imtiaz.hussain@faculty.muet.edu.pk
URL :http://imtiazhussainkalwar.weebly.com/
Lecture-12
Time Domain Analysis of Control systems

## Slide 2: Introduction
In time-domain analysis the response of a dynamic system to an input is expressed as a function of time.
It is possible to compute the time response of a system if the nature of input and the mathematical model of the system are known.
Usually, the input signals to control systems are not known fully ahead of time.
For example, in a radar tracking system, the position and the speed of the target to be tracked may vary in a random fashion.
It is therefore difficult to express the actual input signals mathematically by simple equations.

## Slide 3: Standard Test Signals
The characteristics of actual input signals are a sudden shock, a sudden change, a constant velocity, and constant acceleration.
The dynamic behavior of a system is therefore judged and compared under application of standard test signals – an impulse, a step, a constant velocity, and constant acceleration.
Another standard signal of great importance is a sinusoidal signal.

## Slide 4: Standard Test Signals
Impulse signal
  The impulse signal imitate the sudden shock characteristic of actual input signal.
  If A=1, the impulse signal is called unit impulse signal.
0
t
δ(t)
A

## Slide 5: Standard Test Signals
Impulse signal
Source: English Wikipedia. Iain. Original image: [1]

## Slide 6: Standard Test Signals
Step signal
  The step signal imitate the sudden change characteristic of actual input signal.
  If A=1, the step signal is called unit step signal
0
t
u(t)
A

## Slide 7: Standard Test Signals
Ramp signal
  The ramp signal imitate the constant velocity characteristic of actual input signal.
  If A=1, the ramp signal is called unit ramp signal
0
t
r(t)
r(t)
unit ramp signal
r(t)
ramp signal with slope A

## Slide 8: Standard Test Signals
Parabolic signal
  The parabolic signal imitate the constant acceleration characteristic of actual input signal.
  If A=1, the parabolic signal is called unit parabolic signal.
0
t
p(t)
parabolic signal with slope A
p(t)
Unit parabolic signal
p(t)

## Slide 9: Relation between standard Test Signals
Impulse
Step
Ramp
Parabolic

## Slide 10: Laplace Transform of Test Signals
Impulse
Step

## Slide 11: Laplace Transform of Test Signals
Ramp
Parabolic

## Slide 12: Time Response of Control Systems
System
The time response of any system has two components
  Transient response
  Steady-state response.
Time response of a dynamic system is response to an input expressed as a function of time.

## Slide 13: Time Response of Control Systems
When the response of the system is changed form rest or equilibrium it takes some time to settle down.
Transient response is the response of a system from rest or equilibrium to steady state.
Transient Response
Steady State Response
The response of the system after the transient response is called steady state response.

## Slide 14: Time Response of Control Systems
Transient response dependents upon the system poles only and not on the type of input.
It is therefore sufficient to analyze the transient response using a step input.
The steady-state response depends on system dynamics and the input quantity.
It is then examined using different test signals by final value theorem.

## Slide 15: End of Lecture-12
To download this lecture visit
http://imtiazhussainkalwar.weebly.com/