## Slide 1: Digital Control Systems (DCS)
Dr. Imtiaz Hussain
Associate Professor
Mehran University of Engineering & Technology Jamshoro, Pakistan
email: imtiaz.hussain@faculty.muet.edu.pk
URL :http://imtiazhussainkalwar.weebly.com/
Lecture-14-15-16
Design of Control Systems in Sate Space
Observer Based Approach

## Slide 2: Lecture Outline
Introduction
State Observer
  Topology of Pole Placement (Observer based)
  Full Order State Observer
  Reduced Order state Observer
    Using Transformation Matrix P
    Direct Substitution Method
    Ackermann’s Formula

## Slide 3: Introduction
In the pole-placement approach to the design of control systems, we assumed that all state variables are available for feedback.
In practice, however, not all state variables are available for feedback.
Then we need to estimate unavailable state variables.

## Slide 4: Introduction
Estimation of unmeasurable state variables is commonly called observation.
A device (or a computer program) that estimates or observes the state variables is called a state estimator, state observer, or simply an observer.
There are two types of state observers
  Full Order State Observer
    If the state observer observes all state variables of the system, regardless of whether some state variables are available for direct measurement, it is called a full-order state observer.
  Reduced Order State Observer
    If the state observer observes only those state variables which are not available for direct measurement, it is called a reduced-order state observer.

## Slide 5: Topology of State Feedback Control with Observer Based Approach
State feedback with state observer

## Slide 6: Topology of State Feedback Control with Observer Based Approach
State feedback Control

## Slide 7: Topology of State Feedback Control with Observer Based Approach
State Feedback with observer

## Slide 8: State Observer
A state observer estimates the state variables based on the measurements of the output and control variables.
Here the concept of observability plays an important role.
State observers can be designed if and only if the observability condition is satisfied.

## Slide 9: State Observer
Consider the plant defined by
The mathematical model of the observer is basically the same as that of the plant, except that we include an additional term that includes the estimation error to compensate for inaccuracies in matrices A and B and the lack of the initial error.
The estimation error or observation error is the difference between the measured output and the estimated output.
The initial error is the difference between the initial state and the initial estimated state.

## Slide 10: State Observer
Thus we define the mathematical model of observer to be
Where is estimated state vector, is estimated output and is observer gain matrix.

## Slide 11: Full Order State Observer
The order of the state observer that will be discussed here is the same as that of the plant.
Consider the plant define by following equations
Equation of state observer is given as
To obtain the observer error equation, let us subtract Equation (2) from Equation (1):
(1)
(2)

## Slide 12: Full Order State Observer
Simplifications in above equation yields
Define the difference between and as the error vector e.
Equation (3) can now be written as
(3)

## Slide 13: Full Order State Observer
From above we see that the dynamic behavior of the error vector is determined by the eigenvalues of matrix A-KeC.
If matrix A-KeC is a stable matrix, the error vector will converge to zero for any initial error vector e(0).
That is, will converge to regardless of the values of x(0).
And if the eigenvalues of matrix A-KeC are chosen in such a way that the dynamic behavior of the error vector is asymptotically stable and is adequately fast, then any error vector will tend to zero (the origin) with an adequate speed.

## Slide 14: Full Order State Observer
If the plant is completely observable, then it can be proved that it is possible to choose matrix Ke such that A-KeC has arbitrarily desired eigenvalues.
That is, the observer gain matrix Ke can be determined to yield the desired matrix A-KeC.

## Slide 15: Duality Property
The design of the full-order observer becomes that of determining an appropriate Ke such that A-KeC has desired eigenvalues.
Thus, the problem here becomes the same as the pole-placement problem.
In fact, the two problems are mathematically the same.
This property is called duality.

## Slide 16: Controllable Canonical Form

## Slide 17: Observable Canonical Form

## Slide 18: Duality Property
Consider the system defined by
In designing the full-order state observer, we may solve the dual problem, that is, solve the pole-placement problem for the dual system.
Assuming the control signal to be

## Slide 19: Duality Property
If the dual system is completely state controllable, then the state feedback gain matrix K can be determined such that matrix A*-C*K will yield a set of the desired eigenvalues.
If , ,…, , are the desired eigenvalues of the state observer matrix, then by taking the same as the desired eigenvalues of the state-feedback gain matrix of the dual system, we obtain
Noting that the eigenvalues of A*-C*K and those of A-K*C are the same, we have

## Slide 20: Duality Property
Comparing the characteristic polynomial and the characteristic polynomial for the observer system , we find that Ke and K* are related by
Thus, using the matrix K determined by the pole-placement approach in the dual system, the observer gain matrix Ke for the original system can be determined by using the relationship Ke=K*.

## Slide 21: Observer Gain Matrix
Using Transformation Matrix Q
Direct Substitution Method
Ackermann’s Formula

## Slide 22: Observer Gain Matrix
Using Transformation Matrix Q
Since

## Slide 23: Observer Gain Matrix
Direct Substitution Method

## Slide 24: Observer Gain Matrix
Ackermann’s Formula
For the dual system
Since

## Slide 25: Observer Gain Matrix
Simplifying it further

## Slide 26: Observer Gain Matrix
The feedback signal through the observer gain matrix Ke serves as a correction signal to the plant model to account for the unknowns in the plant.
If significant unknowns are involved, the feedback signal through the matrix Ke should be relatively large.
However, if the output signal is contaminated significantly by disturbances and measurement noises, then the output y is not reliable and the feedback signal through the matrix Ke should be relatively small.

## Slide 27: Observer Gain Matrix
The observer gain matrix Ke depends on the desired characteristic equation
The observer poles must be two to five times faster than the controller poles to make sure the observation error (estimation error) converges to zero quickly.
This means that the observer estimation error decays two to five times faster than does the state vector x.
Such faster decay of the observer error compared with the desired dynamics makes the controller poles dominate the system response.

## Slide 28: Observer Gain Matrix
It is important to note that if sensor noise is considerable, we may choose the observer poles to be slower than two times the controller poles, so that the bandwidth of the system will become lower and smooth the noise.
In this case the system response will be strongly influenced by the observer poles.
If the observer poles are located to the right of the controller poles in the left-half s plane, the system response will be dominated by the observer poles rather than by the control poles.

## Slide 29: Observer Gain Matrix
In the design of the state observer, it is desirable to determine several observer gain matrices Ke based on several different desired characteristic equations.
For each of the several different matrices Ke , simulation tests must be run to evaluate the resulting system performance.
Then we select the best Ke from the viewpoint of overall system performance.
In many practical cases, the selection of the best matrix Ke boils down to a compromise between speedy response and sensitivity to disturbances and noises.

## Slide 30: Example-1
  Consider the system
  We use observer based approach to design state feedback control such that
Design a full-order state observer assume that the desired eigenvalues of the observer matrix are , .

## Slide 31: Example-1
  Let us examine the observability matrix first
Since rank(OM)=2 the given system is completely state observable and the determination of the desired observer gain matrix is possible.

## Slide 32: Example-1 (Method-1)
The given system is already in the observable canonical form. Hence, the transformation matrix Q is I.

## Slide 33: Example-1 (Method-1)
The characteristic equation of the given system is
We have

## Slide 34: Example-1 (Method-1)
The desired characteristic equation of the system is
We have

## Slide 35: Example-1 (Method-1)
Observer gain matrix Ke can be calculated using following formula
Where

## Slide 36: Example-1 (Method-2)
The characteristic equation of observer error matric is
Assuming

## Slide 37: Example-1 (Method-2)
The desired characteristic polynomial is
Comparing coefficients of different powers of s

## Slide 38: Example-1 (Method-3)
Using Ackermann’s formula
Where

## Slide 39: Example-1 (Method-3)

## Slide 40: Example-1 (Method-3)
Using Ackermann’s formula

## Slide 41: Example-1
We get the same Ke regardless of the method employed.
The equation for the full-order state observer is given by

## Slide 42: Example-2
  Design a regulator system for the following plant:
The desired closed-loop poles for this system are at , . Compute the state feedback gain matrix K to place the poles of the system at desired location.
Suppose that we use the observed-state feedback control instead of the actual-state feedback. The desired eigenvalues of the observer matrix are , .
Obtain the observer gain matrix Ke and draw a block diagram for the observed-state feedback control system.

## Slide 43: End of Lectures-14-15-16
To download this lecture visit
http://imtiazhussainkalwar.weebly.com/