## Slide 1: Digital Control Systems (DCS)
Lecture-17-18-19
Introduction to Digital Control Systems
Dr. Imtiaz Hussain
Associate Professor
Mehran University of Engineering & Technology Jamshoro, Pakistan
email: imtiaz.hussain@faculty.muet.edu.pk
URL :http://imtiazhussainkalwar.weebly.com/

## Slide 2: Lecture Outline
Introduction
Difference Equations
Review of Z-Transform
Inverse Z-transform
Relations between s-plane and z-plane
Solution of difference Equations

## Slide 3: Recommended Book
M.S. Fadali, “Digital Control Engineering – Analysis and Design”, Elsevier, 2009. ISBN: 13: 978-0-12-374498-2
Professor of Electrical Engineering
Area of Specialization: Control Systems

## Slide 4: Introduction
Digital control offers distinct advantages over analog control that explain its popularity.
Accuracy: Digital signals are more accurate than their analogue counterparts.
Implementation Errors: Implementation errors are negligible.
Flexibility: Modification of a digital controller is possible without complete replacement.
Speed: Digital computers may yield superior performance at very fast speeds
Cost: Digital controllers are more economical than analogue controllers.

## Slide 5: Structure of a Digital Control System

## Slide 6: Examples of Digital control Systems
Closed-Loop Drug Delivery System

## Slide 7: Examples of Digital control Systems
Aircraft Turbojet Engine

## Slide 8: Difference Equation vs Differential Equation
A difference equation expresses the change in some variable as a result of a finite change in another variable.
A differential equation expresses the change in some variable as a result of an infinitesimal change in another variable.

## Slide 9: Differential Equation
Following figure shows a mass-spring-damper-system. Where y is position, F is applied force D is damping constant and K is spring constant.
Rearranging above equation in following form

## Slide 10: Differential Equation
Rearranging above equation in following form

## Slide 11: Difference Equation
)

## Slide 12: Difference Equations
Difference equations arise in problems where the independent variable, usually time, is assumed to have a discrete set of possible values.
Where coefficients , ,… and , ,… are constant.
is forcing function

## Slide 13: Difference Equations
Example-1: For each of the following difference equations, determine the (a) order of the equation. Is the equation (b) linear, (c) time invariant, or (d) homogeneous?

## Slide 14: Difference Equations
Example-1: For each of the following difference equations, determine the (a) order of the equation. Is the equation (b) linear, (c) time invariant, or (d) homogeneous?
Solution:
The equation is second order.
All terms enter the equation linearly
All the terms if the equation have constant coefficients. Therefore the equation is therefore LTI.
A forcing function appears in the equation, so it is nonhomogeneous.

## Slide 15: Difference Equations
Example-1: For each of the following difference equations, determine the (a) order of the equation. Is the equation (b) linear, (c) time invariant, or (d) homogeneous?
Solution:
The equation is 4th order.
All terms are linear
The second coefficient is time dependent
There is no forcing function therefore the equation is homogeneous.

## Slide 16: Difference Equations
Example-1: For each of the following difference equations, determine the (a) order of the equation. Is the equation (b) linear, (c) time invariant, or (d) homogeneous?
Solution:
The equation is 1st order.
Nonlinear
Time invariant
Homogeneous

## Slide 17: Z-Transform
Difference equations can be solved using classical methods analogous to those available for differential equations.
Alternatively, z-transforms provide a convenient approach for solving LTI equations.
The z-transform is an important tool in the analysis and design of discrete-time systems.
It simplifies the solution of discrete-time problems by converting LTI difference equations to algebraic equations and convolution to multiplication.
Thus, it plays a role similar to that served by Laplace transforms in continuous-time problems.

## Slide 18: Z-Transform
Given the causal sequence {u0, u1, u2, …, uk}, its z-transform is defined as
The variable z −1 in the above equation can be regarded as a time delay operator.

## Slide 19: Z-Transform
Example-2: Obtain the z-transform of the sequence

## Slide 20: Relation between Laplace Transform and Z-Transform
Given the impulse train representation of a discrete-time signal

## Slide 21: Relation between Laplace Transform and Z-Transform
The Laplace Transform of above equation is
And the Z-transform of is given as
Comparing (A) and (B) yields

## Slide 22: Conformal Mapping between s-plane to z-plane
Where .
Then in polar coordinates is given by

## Slide 23: Conformal Mapping between s-plane to z-plane
We will discuss following cases to map given points on s-plane to z-plane.
  Case-1: Real pole in s-plane
  Case-2: Imaginary Pole in s-plane
  Case-3: Complex Poles

## Slide 24: Conformal Mapping between s-plane to z-plane
Case-1: Real pole in s-plane
We know
Therefore

## Slide 25: Conformal Mapping between s-plane to z-plane
When
Case-1: Real pole in s-plane

## Slide 26: Conformal Mapping between s-plane to z-plane
When
Case-1: Real pole in s-plane

## Slide 27: Conformal Mapping between s-plane to z-plane
Consider
Case-1: Real pole in s-plane

## Slide 28: Conformal Mapping between s-plane to z-plane
Case-2: Imaginary pole in s-plane
We know
Therefore

## Slide 29: Conformal Mapping between s-plane to z-plane
Consider
Case-2: Imaginary pole in s-plane

## Slide 30: Conformal Mapping between s-plane to z-plane
When
Case-2: Imaginary pole in s-plane

## Slide 31: Conformal Mapping between s-plane to z-plane
When
Case-2: Imaginary pole in s-plane

## Slide 32: Conformal Mapping between s-plane to z-plane
Anything in the Alias/Overlay region in the S-Plane will be overlaid on the Z-Plane along with the contents of the strip between .

## Slide 33: Conformal Mapping between s-plane to z-plane
In order to avoid aliasing, there must be nothing in this region, i.e. there must be no signals present with radian frequencies higher than w = p/T, or cyclic frequencies higher than f = 1/2T.
Stated another way, the sampling frequency must be at least twice the highest frequency present (Nyquist rate).

## Slide 34: Conformal Mapping between s-plane to z-plane
Case-3: Complex pole in s-plane

## Slide 35: Mapping regions of the s-plane onto the z-plane

## Slide 36: Mapping regions of the s-plane onto the z-plane

## Slide 37: Mapping regions of the s-plane onto the z-plane

## Slide 40: Example-3
Map following s-plane poles onto z-plane assume (T=1). Also comment on the nature of step response in each case.

## Slide 41: z-Transforms of Standard Discrete-Time Signals
The following identities are used repeatedly to derive several important results.

## Slide 42: z-Transforms of Standard Discrete-Time Signals
Unit Impulse
Z-transform of the signal

## Slide 43: z-Transforms of Standard Discrete-Time Signals
Sampled Step
or
Z-transform of the signal

## Slide 44: z-Transforms of Standard Discrete-Time Signals
Sampled Ramp
Z-transform of the signal

## Slide 45: z-Transforms of Standard Discrete-Time Signals
Sampled Parabolic Signal
Then

## Slide 46: Exercise
Find the z-transform of following causal sequences.

## Slide 47: Exercise
Find the z-transform of following causal sequences.
Solution: Using Linearity Property

## Slide 48: Exercise
Find the z-transform of following causal sequences.
Solution: The given sequence is a sampled step starting at k-2 rather than k=0 (i.e. it is delayed by two sampling periods). Using the delay property, we have

## Slide 49: Inverse Z-transform
Long Division: We first use long division to obtain as many terms as desired of the z-transform expansion.
Partial Fraction: This method is almost identical to that used in inverting Laplace transforms. However, because most z-functions have the term z in their numerator, it is often convenient to expand F(z)/z rather than F(z).

## Slide 50: Inverse Z-transform
Example-4: Obtain the inverse z-transform of the function
Solution
1. Long Division

## Slide 51: Inverse Z-transform
1. Long Division
Thus
Inverse z-transform

## Slide 52: Inverse Z-transform
Example-5: Obtain the inverse z-transform of the function
Solution
2. Partial Fractions

## Slide 53: Inverse Z-transform

## Slide 54: Inverse Z-transform
Taking inverse z-transform (using z-transform table)

## Slide 55: Inverse Z-transform
Example-6: Obtain the inverse z-transform of the function
Solution
2. Partial Fractions

## Slide 56: Z-transform solution of Difference Equations
By a process analogous to Laplace transform solution of differential equations, one can easily solve linear difference equations.
  The equations are first transformed to the z-domain (i.e., both the right- and left-hand side of the equation are z-transformed) .
  Then the variable of interest is solved.
  Finally inverse z-transformed is computed.

## Slide 57: Z-transform solution of Difference Equations
Example-7: Solve the linear difference equation
With initial conditions
1. Taking z-transform of given equation
2. Solve for X(z)
Solution

## Slide 58: Z-transform solution of Difference Equations
Then
3. Inverse z-transform

## Slide 59: End of Lectures-17-18-19
To download this lecture visit
http://imtiazhussainkalwar.weebly.com/