## Slide 1: Communication Systems (EE-341)
Dr. Imtiaz Hussain
Associate Professor (Control Systems),
School of Electrical Engineering
DHA Suffa University, Karachi, Pakistan
email: imtiaz.hussain@faculty.muet.edu.pk
URL :http://imtiazhussainkalwar.weebly.com/
Lecture-1
Introduction
Note: I do not claim any originality in these lectures. The contents of this presentation are mostly taken from the book Communication Systems, by Simon Haykin and various other internet sources.
5th Semester (Sec-5A)
Location GF-030
Monday-Wednesday-Friday 11:00 am

## Slide 2: My Introduction
Dr. Imtiaz Hussain (SF-234 Computer Science)
Qualification
  B.E (Electronic Engineering, MUET, Jamshoro, 2003)
  Postgraduate Diploma (PGDip, MUET Jamshoro, Telecom & Control, 2007)
  PhD (Vehicle Dynamics & Control, University of Leeds & University of Salford, Manchester, UK, 2012).

## Slide 3: My Introduction
Employment
  Instrumentation & Control Engineer in couple of Local industries for Six Months
  Lab Lecturer, MUET, Jamshoro (Electronic Engineering, 2004)
  Lecturer, MUET, Jamshoro (Electronic Engineering, 2009)
  Assistant Professor, MUET, Jamshoro (Electronic Engineering, 2012)
  Associate Professor, MUET, Jamshoro (Electronic Engineering, 2015)
  Was appointed as Co-Director Institute of Information & Communication Technologies, MUET, Jamshoro in March 2017.
  Associate Professor, DHA Suffa, (Electrical Engineering, August 2017)

## Slide 4: My Introduction
Achievements
  Recipient of HEC Faculty Development Program Scholarship
  Recipient of HEC overseas Scholarship
  43 Research Publications in National and International Journals and Conferences.
  HEC Approved PhD Supervisor
  Produced 1 PhD in 2016
  Produced 32 M.Phil/ M.Eng
  Supervised Several Undergraduate Projects
  UK’s Best Young Researcher Award (2012), Awarded By IMechE, UK (Institute of Mechanical Engineers UK).

## Slide 5: Objectives of this Course
This course is structured as a senior-level design course emphasizing on
  Fundamental communication principles
  Application of these principles to contemporary analogue and digital communication Systems.
    Such as, Television, Radio, Mobile and satellite communications

## Slide 6: Syllabus
Introduction: Block diagram of a communication system, modes of communication, transmission methods, bandwidth, signal-to-noise ratio
Amplitude Modulation: Double Sideband Suppressed Carrier (DSB-SC) System, Double Sideband Large Carrier (DSB-LC) System, Single Sideband(SSB) System, Vestigial Sideband (VSB) System.
Angle Modulation: Basic concepts of frequency and phase modulation, narrowband and wideband frequency modulation, Spectra and bandwidth of frequency modulated systems, Power in FM systems, demodulation of angle modulated systems.
Pulse Modulation: Pulse Amplitude Modulation (PAM), Pulse Width Modulation (PWM), Pulse Position Modulation (PPM), Pulse Code Modulation (PCM), Laws of Companding, Line Codes, Differential PCM, Delta Modulation.

## Slide 7: Syllabus
Multiplexing: Frequency Division Multiplexing, Time Division Multiplexing, Wavelength Division Multiplexing, an introduction to orthogonal frequency division multiplexing.
Digital Modulation: Amplitude Shift Keying, Frequency Shift Keying, Phase Shift Keying, Quadrature Amplitude Modulation.
Spread Spectrum Techniques: Pseudo binary codes, Direct Sequence spread Spectrum, Frequency hop Spread Spectrum, An introduction to multiple access techniques.
Modems: Classification, Dial-up modems, Digital Subscriber Line (DSL) modems, Cable modems.
Information Theory: Information content of a message, entropy and entropy rate, Channel Capacity, Hartley-Shanon Theorem, Huffmann coding.

## Slide 8: Syllabus
Recommended Books:
B.P Lathi, "Modern Analogue and Digital Communication", Latest Edition, Oxford University Press.
Timosi W., "Electronic Communication Systems", Latest Edition, Pearson Education.
Haykin, S.; “Communication Systems”, Latest Edition, John Wiley & Sons.

## Slide 9: Telecommunication
Telecommunication aka Communication
  What is it?
    Process by which information is exchanged
    The word Telecommunication is merger of two words Tele + communications, which means communication at distance!
  What are the forms of communication?
    Audio, visual, audio/visual, radio, electrical signal over copper etc.

## Slide 10: Basic Elements of a Communication System
Every communication system consists of
  A transmitter
  A receiver
  A medium over which transmission occurs
  Practical communication systems are more complex.
Transmitter
Receiver
Communication medium
Noise

## Slide 11: Basic Elements of a Communication System
Transmitter
  “transmit” = send information to the receiver
  Uses the most suitable method to convey information
    Method depends upon the communication medium
      Audio
      Visual/Video
      Hand gestures, smoke signals…
Communication medium
  Literally, medium of communication
    Wired and wireless
Receiver
  “receiver” = receive/recover information from the transmitter
  Receiver designed according to the transmitter

## Slide 12: Classification of Communication systems
There are many ways to differentiate one communication system from other! (Classification).
For example
  Wired and Wireless
  Electrical and optical
  Narrowband and wideband
  Based on modes: Simplex, Half duplex and Full duplex

## Slide 13: How do we communicate these days…
PTCL landline telephones
PTCL EVO (wireless broadband)
DSL
LAN
Cable TV
AM/ FM radio
GSM/GPRS/EDGE/H+
WLAN

## Slide 14: History of “Electronic” Communications
1793 | Claude Chappe invents the first optical telegraph
1831 | Joseph Henry invents the first electric telegraph
1835 | Samuel Morse invents Morse code
1843 | Samuel Morse invents the first long distance electric telegraph line
1876 | Alexander Graham Bell made the first telephone call to his assistant with the words, “Mr. Watson, come here, I want you.
1889 | Almon Strowger developed the first automatic (electromechanical) telephone exchange.
1894 | Guglielmo Marconi improves wireless telegraphy.
1902 | Guglielmo Marconi transmits radio signals from Cornwall, UK to Newfoundland, USA i.e. the first radio signal across the Atlantic ocean.
1917 | AT&T’s system sends four telephone calls at once along a single pair of lines.

## Slide 15: History of “Electronic” Communications
1923 | Primitive television invented by Vladimir Kosma Zworykin
1925 | John Baird transmits first experimental television signal
1927 | First television broadcast in UK
1930 | “Golden Age of Radio” First television broadcast in USA
1944 | AT&T’s L1 system transmits 600 calls at once over a coaxial cable.
1957 | USSR launches Sputnik-1 satellite in space
1958 | USA launches Score satellite in space
1961 | AT&T begins digitized phone calls for its T1 system.
1963 | The first communications geostationary satellite Syncom 2, was launched by NASA.
1969 | ARPANET – first internet started
1972 | Robert Metcalfe worked out a LAN system called Ethernet.
1979 | First cellular phone communication starts in Japan

## Slide 16: History of “Electronic” Communications-3
1983 | Cellular phone communication starts in USA
1989 | PTAT-1 the first private trans-Atlantic fiber optic cable carries two third of all trans-Atlantic data traffic.
1991 | First GSM call made in Finland
1992 | First SMS made

## Slide 17: Transmission Modes - Modes of Communications
One way
  Simplex
  One person talks, the other listens
    FM radio
    Satellite TV
Two way
  Half Duplex
  Two people can talk but one at a time
    Walkie-talkie
Both way
  Full duplex
  Two people can talk simultaneously
    GSM phone call
    PTCL phone call

## Slide 18: Communication Tasks
Some common tasks performed by modern communication systems include:
  Transmission system utilization
  Addressing
  Routing
  Signal Generation
  Recovery
  Security (encryption/decryption)
  Error detection and correction

## Slide 19: Communication Tasks
Transmission system utilization
  It is actually the efficient use of transmission facilities that are shared among a number of connected devices.
Addressing
  When a transmission system is shared by more than two devices, every device is issued with its unique address by which it can be located over the network.
Routing
  The term routing refers to steering the data to the desired destination system. During the routing process. It is assured that the data must be received by the intended system(s) only.

## Slide 20: Communication Tasks
Signal Generation
  The signal generation process ensures that
    i) the signal is capable to be propagated through the channel.
    ii) the signal is interpretable by the receiver as valid data.
Recovery
  It is generally the case with the digital communication system that when a link is terminated unintentionally/abnormally, during the conversation, and established again, the data must be received from the point where the link was broken down. This process is called recovery.
Security
  Security refers to protection of data to be taped down/hacked by any unauthorized user of the network.
Error correction & detection
  These mechanisms are required in such situations where errors cannot be tolerated.

## Slide 21: The Electromagnetic Theory
The James Clerk Maxwell in 1865 predicted that heat, light, and electricity are propagated in free space at the speed of light as electromagnetic disturbances.

## Slide 24: Signals-Basics
A signal is a function which represents a physical quantity
  A function of one, two or more variables
  For example,
    Temperature in Karachi during a given week
      Depends upon?
    Rainfall in Pakistan during the year
      Depends upon?
    Your voice signals is a function of time and frequency.

## Slide 25: Signals-Basics
Various types of signals in communications
  Electrical signals
    Voltages and currents
  Acoustic signals
    Sound
  Video signals
    Intensity level of a pixel (camera, video) over time
  But, for enabling an electronic communication system, we convert all signals into electrical signals
    Using various kinds of transducers

## Slide 26: Signals-Basics
Consider a signal
So all information is represented by one or more of these parameters
Amplitude
Frequency
Phase

## Slide 27: Some key terms
Amplitude
  Measure of the strength of the signal
Frequency
  Number of oscillations per second
  Hertz
Bandwidth
  Range of frequencies occupied by a signal
    Our voice signal occupies the frequencies between 300-3400 Hz

## Slide 28: Signals-Basics
A microphone converts the voice signal from mechanical signal into an electrical signal
Similarly, a digital camera converts a picture into digital images
  Sensors

## Slide 29: Analogue and Digital Signals
Analogue signals
  Continuous in time and continuous in amplitude
  Most signals in the real world are continuous time
x(t)
t

## Slide 30: Analogue and Digital Signals
Digital signals
  Discrete in time and usually discrete in terms of amplitude too
  Some real world signals are discrete, computer signals are always discrete
x[n]
n

## Slide 31: System-Basics
“Systems” process input signals to produce output signals
  Manipulate signals
Example,
  An MP3 player is a system because it converts data (MP3 song) into audio signals
  A communication system

## Slide 32: Sine and Cosine signal
Sinusoidal signals
  Start from “0”
    sin(2πf x 0) = 0, @t=0
Cosinusoidal (cosine) signals
  Start from “1”
    cos(2πf x 0) = 1, @t=0

## Slide 33: Some important terms
Time Period
Trough
Crest
Wavelength

## Slide 34: Some important terms
Crest
  Indicates largest value of a signal
Trough
  Indicates smallest value of a signal
Time period
  Time taken by the signal to complete one cycle
  Measured in seconds
Frequency
  Number of cycles completed by the signal in one second
  Measured in Hertz

## Slide 35: Some important terms
Wavelength
  Distance (spatial i.e. in meters) between two successive crests or troughs
  Distance travelled by a signal in one cycle
Wavelength

## Slide 36: Some important terms
For wireless communication, velocity is taken as 3x108 m/s
For wireline communication (electrical), velocity is taken as 2x108 m/s

## Slide 37: Find the amplitude, freq & phase of the following signals
Amplitude
Frequency
Phase

## Slide 38: Noise
Noise is a random signal (no particular shape or pattern)
It is an undesirable signal
  Because it corrupts information!
Noise usually enters the communication system via the communicating medium
  But it could be locally generated as well.

## Slide 39: Time-domain & frequency-domain plots
Most signals of our interest are dependent on time and frequency
  At the same time
Therefore, we have two different kinds of plots
  Time-domain plots
    Give information about the time dependent properties
  Frequency-domain plots
    Give information about the frequency dependent properties

## Slide 40: Example-1
I Complete cycle in 1 sec

## Slide 41: Example-2
I Complete cycle in 0.5 sec

## Slide 42: Example-3

## Slide 43: Example-4

## Slide 44: Signals and Spectra
Electrical communication signals are time-varying quantities such as voltage or current.
Although a signal physically exists in the time domain, we can also represent it in the frequency domain where we view the signal as consisting of sinusoidal components at various frequencies.

## Slide 45: Signals and Spectra
This frequency-domain description is called the spectrum.

## Slide 46: Spectrum & Bandwidth
Spectrum
  range of frequencies contained in signal
Bandwidth
  width of spectrum

## Slide 47: Spectrum & Bandwidth
Bandwidth (BW)=(6000-1000)=5000Hz=5KHz
Range of Frequencies?
Bandwidth?

## Slide 48: Spectrum of Pure Sine wave
Power Line Frequency

## Slide 49: Signals and Spectra
All non-sinusoidal complex waveforms are made up of a number of sine waves.
e.g Square wave

## Slide 50: Signals and Spectra
All non-sinusoidal complex waveforms are made up of a number of sine waves.
e.g. Square wave

## Slide 51: Signals and Spectra
Examples of complex waveforms

## Slide 52: Fourier Series
Any Periodic Signal can be expressed as Fourier series expansion.
Where,

## Slide 53: Fourier Series of Rectangular Wave

## Slide 54: Fourier Series of Rectangular Wave

## Slide 55: Fourier Series of Rectangular Wave
Thus

## Slide 56: Fourier Series of Rectangular Wave

## Slide 57: Fourier Series of Triangular Wave

## Slide 58: Fourier Series of Triangular Wave

## Slide 59: Fourier Series of Triangular Wave

## Slide 60: Fourier Series of Triangular Wave

## Slide 61: Fourier Series of Triangular Wave

## Slide 62: Fourier Series of Triangular Wave

## Slide 63: Acknowledgements
Dr. Faheem Aziz
Engr. Syed M. Zafi Shah
Engr. Umair Mujtaba Qureshi

## Slide 64: End of Lecture-1
To download this lecture visit
http://imtiazhussainkalwar.weebly.com/