## Slide 1: Feedback Control Systems (FCS)
Dr. Imtiaz Hussain
email: imtiaz.hussain@faculty.muet.edu.pk
URL :http://imtiazhussainkalwar.weebly.com/
Lecture-21-22-23
Frequency Response Analysis

## Slide 2: Introduction
Frequency response is the steady-state response of a system to a sinusoidal input.
In frequency-response methods, the frequency of the input signal is varied over a certain range and the resulting response is studied.
System

## Slide 3: The Concept of Frequency Response
In the steady state, sinusoidal inputs to a linear system generate sinusoidal responses of the same frequency.
Even though these responses are of the same frequency as the input, they differ in amplitude and phase angle from the input.
These differences are functions of frequency.

## Slide 4: The Concept of Frequency Response
Sinusoids can be represented as complex numbers called phasors.
The magnitude of the complex number is the amplitude of the sinusoid, and the angle of the complex number is the phase angle of the sinusoid.
Thus can be represented as
where the frequency, ω, is implicit.

## Slide 5: The Concept of Frequency Response
A system causes both the amplitude and phase angle of the input to be changed.
Therefore, the system itself can be represented by a complex number.
Thus, the product of the input phasor and the system function yields the phasor representation of the output.

## Slide 6: The Concept of Frequency Response
Consider the mechanical system.
If the input force, f(t), is sinusoidal, the steady-state output response, x(t), of the system is also sinusoidal and at the same frequency as the input.

## Slide 7: The Concept of Frequency Response
Assume that the system is represented by the complex number
The output is found by multiplying the complex number representation of the input by the complex number representation of the system.

## Slide 8: The Concept of Frequency Response
Thus, the steady-state output sinusoid is
Mo(ω) is the magnitude response and Φ(ω) is the phase response. The combination of the magnitude and phase frequency responses is called the frequency response.

## Slide 9: Frequency Domain Plots
Bode Plot
Nyquist Plot
Nichol’s Chart

## Slide 10: Bode Plot
A Bode diagram consists of two graphs:
  One is a plot of the logarithm of the magnitude of a sinusoidal transfer function.
  The other is a plot of the phase angle.
  Both are plotted against the frequency on a logarithmic scale.

## Slide 12
Decade

## Slide 13: Basic Factors of a Transfer Function
The basic factors that very frequently occur in an arbitrary transfer function are
  Gain K
  Integral and Derivative Factors (jω)±1
  First Order Factors (jωT+1)±1
  Quadratic Factors

## Slide 14: Basic Factors of a Transfer Function
  Gain K
The log-magnitude curve for a constant gain K is a horizontal straight line at the magnitude of 20 log(K) decibels.
The phase angle of the gain K is zero.
The effect of varying the gain K in the transfer function is that it raises or lowers the log-magnitude curve of the transfer function by the corresponding constant amount, but it has no effect on the phase curve.

## Slide 15
-15
-5
5
15
Magnitude (decibels)
Frequency (rad/sec)
0.1
1
10
100
103
104
105
106
107
108
109

## Slide 16
-90o
-300
30o
90o
Phase (degrees)
Frequency (rad/sec)
0.1
1
10
100
103
104
105
106
107
108
109
0o

## Slide 17: Basic Factors of a Transfer Function
  Integral and Derivative Factors (jω)±1
Derivative Factor
Magnitude
Phase
ω | 0.1 | 0.2 | 0.4 | 0.5 | 0.7 | 0.8 | 0.9 | 1
db | -20 | -14 | -8 | -6 | -3 | -2 | -1 | 0
Slope=20db/decade
Slope=6b/octave

## Slide 18
-30
-10
10
30
Magnitude (decibels)
Frequency (rad/sec)
0.1
1
10
100
103
104
105
106
107
108
109
0
-20

## Slide 19
-180o
-600
60o
180o
Phase (degrees)
Frequency (rad/sec)
0.1
1
10
100
103
104
105
106
107
108
109
0o
900

## Slide 20: Basic Factors of a Transfer Function
  Integral and Derivative Factors (jω)±1
When expressed in decibels, the reciprocal of a number differs from its value only in sign; that is, for the number N,
Magnitude
Therefore, for Integral Factor the slope of the magnitude line would be same but with opposite sign (i.e -6db/octave or -20db/decade).
Phase

## Slide 21
-30
-10
10
30
Magnitude (decibels)
Frequency (rad/sec)
0.1
1
10
100
103
104
105
106
107
108
109
0
20

## Slide 22
-180o
-600
60o
180o
Phase (degrees)
Frequency (rad/sec)
0.1
1
10
100
103
104
105
106
107
108
109
0o
-900

## Slide 23: Basic Factors of a Transfer Function
  First Order Factors (jωT+1)
  For Low frequencies ω<<1/T
  For high frequencies ω>>1/T

## Slide 24: Basic Factors of a Transfer Function
  First Order Factors (jωT+1)

## Slide 25
-30
-10
10
30
Magnitude (decibels)
Frequency (rad/sec)
0.1
1
10
100
103
104
105
106
107
108
109
0
20
ω=3
6 db/octave
20 db/decade

## Slide 26
-90o
-300
30o
90o
Phase (degrees)
Frequency (rad/sec)
0.1
1
10
100
103
104
105
106
107
108
109
0o
45o

## Slide 27: Basic Factors of a Transfer Function
  First Order Factors (jωT+1)-1
  For Low frequencies ω<<1/T
  For high frequencies ω>>1/T

## Slide 28: Basic Factors of a Transfer Function
  First Order Factors (jωT+1)-1

## Slide 29
-30
-10
10
30
Magnitude (decibels)
Frequency (rad/sec)
0.1
1
10
100
103
104
105
106
107
108
109
0
-20
ω=3
-6 db/octave
-20 db/decade

## Slide 30
-90o
-300
30o
90o
Phase (degrees)
Frequency (rad/sec)
0.1
1
10
100
103
104
105
106
107
108
109
0o
-45o

## Slide 31: Example#1
Draw the Bode Plot of following Transfer function.
Solution:
The transfer function contains
  Gain Factor (K=2)
  Derivative Factor (s)
  1st Order Factor in denominator (0.1s+1)-1

## Slide 32: Example#1
  Gain Factor (K=2)
  Derivative Factor (s)
  1st Order Factor in denominator (0.1s+1)

## Slide 33
-30
-10
10
30
Magnitude (decibels)
Frequency (rad/sec)
0.1
1
10
100
103
104
105
106
107
108
109
0
-20
K=2
20 db/decade
-20 db/decade

## Slide 34
-30
-10
10
30
Magnitude (decibels)
Frequency (rad/sec)
0.1
1
10
100
103
104
105
106
107
108
109
0
-20
20 db/decade
-20 db/decade+20db/decade

## Slide 35: Example#1
ω | 0.1 | 1 | 5 | 10 | 20 | 40 | 70 | 100 | 1000 | ∞
Φ(ω) | 89.4 | 84.2 | 63.4 | 45 | 26.5 | 14 | 8 | 5.7 | 0.5 | 0

## Slide 36
-90o
-300
30o
90o
Phase (degrees)
Frequency (rad/sec)
0.1
1
10
100
103
104
105
106
107
108
109
0o
-45o
ω | 0.1 | 1 | 5 | 10 | 20 | 40 | 70 | 100 | 1000 | ∞
Φ(ω) | 89.4 | 84.2 | 63.4 | 45 | 26.5 | 14 | 8 | 5.7 | 0.5 | 0

## Slide 38: Example#2
Solution:

## Slide 39: Basic Factors of a Transfer Function
  Quadratic Factors
  For Low frequencies ω<< ωn
  For high frequencies ω>> ωn

## Slide 40: Minimum-Phase & Non-minimum Phase Systems

## Slide 41: Minimum-Phase & Non-minimum Phase Systems

## Slide 42: Minimum-Phase & Non-minimum Phase Systems

## Slide 43: Minimum-Phase & Non-minimum Phase Systems

## Slide 44: Minimum-Phase & Non-minimum Phase Systems

## Slide 45: Minimum-Phase & Non-minimum Phase Systems
Transfer functions having neither poles nor zeros in the right-half s plane are minimum-phase transfer functions.
Whereas, those having poles and/or zeros in the right-half s plane are non-minimum-phase transfer functions.

## Slide 46: Relative Stability
  Phase crossover frequency (ωp) is the frequency at which the phase angle of the open-loop transfer function equals –180°.
  The gain crossover frequency (ωg) is the frequency at which the magnitude of the open loop transfer function, is unity.
The gain margin (Kg) is the reciprocal of the magnitude of G(jω) at the phase cross over frequency.
  The phase margin (γ) is that amount of additional phase lag at the gain crossover frequency required to bring the system to the verge of instability.

## Slide 47: Relative Stability

## Slide 48
Gain cross-over point
ωg
Phase cross-over point
ωp

## Slide 49
ωp
Gain Margin
Unstable Stable
Stable
Unstable Stable
Stable
ωg
Phase Margin

## Slide 50: Example#3
Obtain the phase and gain margins of the system shown in following figure for the two cases where K=10 and K=100.

## Slide 52: End of Lectures-21-22-23
To download this lecture visit
http://imtiazhussainkalwar.weebly.com/