## Slide 1: Feedback Control Systems (FCS)
Dr. Imtiaz Hussain
email: imtiaz.hussain@faculty.muet.edu.pk
URL :http://imtiazhussainkalwar.weebly.com/
Lecture-34-35
Modern Control Theory

## Slide 2: Introduction
The transition from simple approximate models, which are easy to work with, to more realistic models produces two effects.
  First, a large number of variables must be included in the models.
  Second, a more realistic model is more likely to contain nonlinearities and time-varying parameters.
  Previously ignored aspects of the system, such as interactions with feedback through the environment, are more likely to be included.

## Slide 3: Introduction
Most classical control techniques were developed for linear constant coefficient systems with one input and one output(perhaps a few inputs and outputs).
The language of classical techniques is the Laplace or Z-transform and transfer functions.
When nonlinearities and time variations are present, the very basis for these classical techniques is removed.
Some successful techniques such as phase-plane methods, describing functions, and other methods, have been developed to alleviate this shortcoming.

## Slide 4: Introduction
The state variable approach of modern control theory provides a uniform and powerful methods of representing systems of arbitrary order, linear or nonlinear, with time-varying or constant coefficients.
It provides an ideal formulation for computer implementation and is responsible for much of the progress in optimization theory.
The advantages of using matrices when dealing with simultaneous equations of various kinds have long been appreciated in applied mathematics.
The field of linear algebra also contributes heavily to modern control theory.

## Slide 5: Introduction
Conventional control theory is based on the input–output relationship, or transfer function approach.
Modern control theory is based on the description of system equations in terms of n first-order differential equations, which may be combined into a first-order vector-matrix differential equation.
The use of vector-matrix notation greatly simplifies the a mathematical representation of systems of equations.
The increase in the number of state variables, the number of inputs, or the number of outputs does not increase the complexity of the equations.

## Slide 6: State Space Representation
State of a system: We define the state of a system at time t0 as the amount of information that must be provided at time t0, which, together with the input signal u(t) for t  t0, uniquely determine the output of the system for all t  t0.
This representation transforms an nth order difference equation into a set of n 1st order difference equations.
State Space representation is not unique.
Provides complete information about all the internal signals of a system.

## Slide 7: State Space Representation
Suitable for both linear and non-linear systems.
Software/hardware implementation is easy.
A time domain approach.
Suitable for systems with non-zero initial conditions.
Transformation From Time domain to Frequency domain and Vice Versa is possible.

## Slide 8: Definitions
State Variable: The state variables of a dynamic system are the smallest set of variables that determine the state of the dynamic system.
State Vector: If n variables are needed to completely describe the behaviour of the dynamic system then n variables can be considered as n components of a vector x, such a vector is called state vector.
State Space: The state space is defined as the n-dimensional space in which the components of the state vector represents its coordinate axes.

## Slide 9: Definitions
Let x1 and x2 are two states variables that define the state of the system completely .
Two Dimensional State space
State (t=t1)
State
Vector
State space of a Vehicle
Velocity
Position
State (t=t1)

## Slide 10: State Space Representation
An electrical network is given in following figure, find a state-space representation if the output is the current through the resistor.

## Slide 11: State Space Representation
Step-1: Select the state variables.
Step-2: Apply network theory, such as Kirchhoff's voltage and current laws, to obtain ic and vL in terms of the state variables, vc and iL.
Applying KCL at Node-1
(1)

## Slide 12: State Space Representation
Step-2: Apply network theory, such as Kirchhoff's voltage and current laws, to obtain ic and vL in terms of the state variables, vc and iL.
Applying KVL at input loop
Step-3: Write equation (1) & (2) in standard form.
(2)
State Equations

## Slide 13: State Space Representation

## Slide 14: State Space Representation
Step-4: The output is current through the resistor therefore, the output equation is

## Slide 15: State Space Representation
Where,
x(t) --------------- State Vector
A (nxn) ---------------- System Matrix
B (nxp) ----------------- Input Matrix
u(t) --------------- Input Vector
Where,
y(t) -------------- Output Vector
C (qxn) ---------------- Output Matrix
D ----------------- Feed forward Matrix

## Slide 16: Example-1
Consider RLC Circuit Represent the system in Sate Space and find (if L=1H, R=3Ω and C=0.5 F):
  State Vector
  System Matrix
  Input Matrix & Input Vector
  Output Matrix & Output Vector
Vc
+
-
+
-
Vo
iL
Choosing vc and iL as state variables

## Slide 17: Example-1 (cont...)
State Equation
Output Equation

## Slide 18: Example-2
Consider the following system
K
M
B
f(t)
x(t)
Differential equation of the system is:

## Slide 19: Example-2
As we know
Choosing x and v as state variables

## Slide 20: Example-2
If velocity v is the out of the system then output equation is given as

## Slide 21: Example-3
Find the state equations of following mechanical translational system.
System equations are:

## Slide 22: Example-3
Now
Choosing x1, v1, x2, v2 as state variables

## Slide 23: Example-3
In Standard form

## Slide 24: Example-3
In Vector-Matrix form

## Slide 25: Example-3
If x1 and v2 are the outputs of the system then

## Slide 26: Eigenvalues & Eigen Vectors
The eigenvalues of an nxn matrix A are the roots of the characteristic equation.
Consider, for example, the following matrix A:

## Slide 27: Eigen Values & Eigen Vectors

## Slide 28: Example#4
Find the eigenvalues if
  K = 2
  M=10
  B=3

## Slide 29: Frequency Domain to time Domain Conversion
Transfer Function to State Space
K
M
B
f(t)
x(t)
Differential equation of the system is:
Taking the Laplace Transform of both sides and ignoring
Initial conditions we get

## Slide 30
The transfer function of the system is
State Space Representation:

## Slide 31
……………………………. (1)
……………………………. (2)
From equation (2)
……………………………. (3)
Draw a simulation diagram of equation (1) and (3)
1/s
1/s
F(s)
X(s)
-K/M
-B/M
P(s)
1/M

## Slide 32
1/s
1/s
F(s)
X(s)
-K/M
-B/M
P(s)
Let us assume the two state variables are x1 and x2.
These state variables are represented in phase variable form as given below.
State equations can be obtained from state diagram.
The output equation of the system is
1/M

## Slide 34: Example#5
Obtain the state space representation of the following Transfer function.

## Slide 35: End of Lectures-34-35
To download this lecture visit
http://imtiazhussainkalwar.weebly.com/