## Slide 1: Power Electronics
Dr. Imtiaz Hussain
Assistant Professor
email: imtiaz.hussain@faculty.muet.edu.pk
URL :http://imtiazhussainkalwar.weebly.com/
Lecture-3
Power Electronic Devices
Power Diodes

## Slide 2: Lecture Outline
Power Electronic Devices
Diode
  Small Signal Diode
  Power Diode
Switching characteristics of power diode
Types of Diodes

## Slide 3: Power Electronic Devices
The power Electronic devices provides the utility of switching.
The flow of power through these devices can be controlled via small currents.
Power electronics devices differ from ordinary electronics devices in terms of their characteristics.

## Slide 4: Power Electronic Devices
Power Semiconductor Devices can be classified into three groups according to their degree of controllability.
  Diodes (on and off controlled by power circuit)
  Thyristors (latched on by control signal but must be turned off by power circuit)
  Controllable Switches (turned on and off by control signal)

## Slide 5: Diode
A p-n junction diode is formed by placing p and n type semiconductor materials in intimate contact on an atomic scale.

## Slide 6
The PN Junction in Steady State
P
n
- - - - - -
- - - - - -
- - - - - -
- - - - - -
- - - - - -
+ + + + + +
+ + + + + +
+ + + + + +
+ + + + + +
+ + + + + +
Space Charge Region
ionized acceptors
ionized donors
E-Field
+
+
_
_
h+ drift
h+ diffusion
e- diffusion
e- drift
=
=
Na
Nd
Metallurgical Junction

## Slide 7
Thermal Equilibrium
Reverse Bias

## Slide 8
Forward Bias

## Slide 9: Diode Characteristics

## Slide 10: Diode Equation
Where,
Is = Reverse saturation current ( Amps)
v = Applied forward voltage across the device (volts)
q = Change of an electron
k = Boltzmann's constant
T = Temperature in Kelvin

## Slide 11: Power Diode
Power semiconductor diode is the “power level” counter part of the “low power signal diodes”.
The symbol of the Power diode is same as signal level diode. However, the construction and packaging is different.

## Slide 12: Power Diode
Power dides are required to carry up to several KA of current under forward bias condition and block up to several KV under reverse biased condition.
Large blocking voltage requires wide depletion layer.
This requirement will be satisfied in a lightly doped p-n junction diode of sufficient width to accommodate the required depletion layer.
Such a construction, however, will result in a device with high resistively in the forward direction.
If forward resistance (and hence power loss) is reduced by increasing the doping level, reverse break down voltage will reduce.

## Slide 13: Power Diode
These extreme requirements call for important structural changes in a power diode which significantly affect their operating characteristics.
This apparent contradiction in the requirements of a power diode is resolved by introducing a lightly doped “drift layer” of required thickness between two heavily doped p and n layers.

## Slide 14: Switching Characteristics of Power Diodes
Power Diodes take finite time to make transition from reverse bias to forward bias condition (switch ON) and vice versa (switch OFF).
Behavior of the diode current and voltage during these switching periods are important due to the following reasons.
  Severe over voltage / over current may be caused by a diode switching at different points in the circuit using the diode.
  Voltage and current exist simultaneously during switching operation of a diode. Therefore, every switching of the diode is associated with some energy loss. At high switching frequency this may contribute significantly to the overall power loss in the diode.

## Slide 15: Turn On Characteristics
Diodes are often used in circuits with di/dt limiting inductors.
The rate of rise of the forward current through the diode during Turn ON has significant effect on the forward voltage drop characteristics.

## Slide 16: Turn On Characteristics
It is observed that the forward diode voltage during turn ON may transiently reach a significantly higher value Vfr compared to the steady slate voltage drop at the steady current IF.
Forward recovery time, tFR is the time required for the diode voltage to drop to a particular value after the forward current starts to flow.

## Slide 17: Turn Off Characteristics
The diode current does not stop at zero, instead it grows in the negative direction to Irr called “peak reverse recovery current” which can be comparable to IF.
Voltage drop across the diode does not change appreciably from its steady state value till the diode current reaches reverse recovery level.

## Slide 18: Turn Off Characteristics
The reverse recovery characteristics shown is typical of a particular type of diodes called “normal recovery” or “soft recovery” diode.
The total recovery time (trr) in this case is a few tens of microseconds.

## Slide 19: Turn Off Characteristics
This is acceptable for line frequency rectifiers (these diodes are also called rectifier grade diodes).
High frequency circuits (e.g PWM inverters) demand faster diode recovery.

## Slide 20: Types of Diodes
Depending on the application requirement various types of diodes are available.
  Schottky Diode
  Fast Recovery Diode
  Line Frequency Diode

## Slide 21: Types of Diodes
  Schottky Diode
  These diodes are used where a low forward voltage drop (typically 0.3 v) is needed.
  These diodes are limited in their blocking voltage capabilities to 50v- 100v.

## Slide 22: Types of Diodes
  Fast Recovery Diode
  These diodes are designed to be used in high frequency circuits in combination with controllable switches where a small reverse recovery time is needed.
  At power levels of several hundred volts and several hundred amperes such diodes have trr rating of less than few microseconds.

## Slide 23: Types of Diodes
  Line Frequency Diode
  The on state of these diodes is designed to be as low as possible.
  As a consequence they have large trr, which are acceptable for line frequency applications.

## Slide 24: Comparison between different types of Diodes
General Purpose Diodes | Fast Recovery Diodes | Schottky Diodes
Up to 6000V & 3500A | Up to 6000V and 1100A | Up to 100V and 300A
Reverse recovery time – High | Reverse recovery time – Low | Reverse recovery time – Extremely low.
24

## Slide 25
General Purpose Diodes | Fast Recovery Diodes | Schottky Diodes
Turn off time – High | Turn off time – Low | Turn off time – Extremely low
Switching frequency – Low (Max 1KHz) | Switching frequency – High (Max 20KHz) | Switching frequency – Very high. (Max 30KHz)
25
Comparison between different types of Diodes

## Slide 26: End of Lecture-3
To download this lecture visit
http://imtiazhussainkalwar.weebly.com/