## Slide 1: Modern Control Systems (MCS)
Dr. Imtiaz Hussain
Assistant Professor
email: imtiaz.hussain@faculty.muet.edu.pk
URL :http://imtiazhussainkalwar.weebly.com/
Lecture-8-9
Lag Compensation

## Slide 2: Lecture Outline
Introduction to lag compensation
Electronic Lag Compensator
Mechanical Lag Compensator
Electrical Lag Compensator
Design Procedure of Lag Compensator
Examples

## Slide 3: Lag Compensation
Lag compensation is used to improve the steady state error of the system.
Generally Lag compensators are represented by following transfer function
Or
Where is gain of lag compensator.
, ()
, ()

## Slide 4: Lag Compensation
, ()

## Slide 5: Lag Compensation
Consider the problem of finding a suitable compensation network for the case where the system exhibits satisfactory transient-response characteristics but unsatisfactory steady-state characteristics.
Compensation in this case essentially consists of increasing the open loop gain without appreciably changing the transient-response characteristics.
This means that the root locus in the neighborhood of the dominant closed-loop poles should not be changed appreciably, but the open-loop gain should be increased as much as needed.

## Slide 6: Lag Compensation
To avoid an appreciable change in the root loci, the angle contribution of the lag network should be limited to a small amount, say less than 5°.
To assure this, we place the pole and zero of the lag network relatively close together and near the origin of the s plane.
Then the closed-loop poles of the compensated system will be shifted only slightly from their original locations. Hence, the transient-response characteristics will be changed only slightly.

## Slide 7: Lag Compensation
Consider a lag compensator Gc(s), where
If we place the zero and pole of the lag compensator very close to each other, then at s=s1 (where s1 is one of the dominant closed loop poles) then the magnitudes and are almost equal, or
, ()

## Slide 8: Lag Compensation
To make the angle contribution of the lag portion of the compensator small, we require
This implies that if gain of the lag compensator is set equal to 1, the alteration in the transient-response characteristics will be very small, despite the fact that the overall gain of the open-loop transfer function is increased by a factor of , where >1.

## Slide 9: Lag Compensation
If the pole and zero are placed very close to the origin, then the value of can be made large.
A large value of may be used, provided physical realization of the lag compensator is possible.
It is noted that the value of T must be large, but its exact value is not critical.
However, it should not be too large in order to avoid difficulties in realizing the phase-lag compensator by physical components.

## Slide 10: Lag Compensation
An increase in the gain means an increase in the static error constants.
If the open loop transfer function of the uncompensated system is G(s), then the static velocity error constant Kv of the uncompensated system is
Then for the compensated system with the open-loop transfer function Gc(s)G(s) the static velocity error constant becomes

## Slide 11: Lag Compensation
The main negative effect of the lag compensation is that the compensator zero that will be generated near the origin creates a closed-loop pole near the origin.
This closed loop pole and compensator zero will generate a long tail of small amplitude in the step response, thus increasing the settling time.

## Slide 12: Electronic Lag Compensator
The configuration of the electronic lag compensator using operational amplifiers is the same as that for the lead compensator shown in following figure.

## Slide 13: Electronic Lag Compensator
Pole-zero Configuration of Lag Compensator

## Slide 14: Electrical Lag Compensator
Following figure lag compensator realized by electrical network.

## Slide 15: Electrical Lag Compensator
Then the transfer function becomes

## Slide 16: Electrical Lag Compensator
If an RC circuit is used as a lag compensator, then it is usually necessary to add an amplifier with an adjustable gain so that the transfer function of compensator is

## Slide 17: Mechanical Lag Compensator (Home Work)

## Slide 18: Design Procedure
The procedure for designing lag compensators by the root-locus method may be stated as follows.
We will assume that the uncompensated system meets the transient-response specifications by simple gain adjustment.
If this is not the case then we need to design a lag-lead compensator which we will discuss in next few classes.

## Slide 19: Design Procedure
Step-1
  Draw the root-locus plot for the uncompensated system whose open-loop transfer function is G(s).
  Based on the transient-response specifications, locate the dominant closed-loop poles on the root locus.

## Slide 20: Design Procedure
Step-2
  Assume the transfer function of the lag compensator to be given by following equation
  Then the open-loop transfer function of the compensated system becomes Gc(s)G(s).
=

## Slide 21: Design Procedure
Step-3
  Evaluate the particular static error constant specified in the problem.
  Determine the amount of increase in the static error constant necessary to satisfy the specifications.

## Slide 22: Design Procedure
Step-4
  Determine the pole and zero of the lag compensator that produce the necessary increase in the particular static error constant without appreciably altering the original root loci.
  The ratio of the value of gain required in the specifications and the gain found in the uncompensated system is the required ratio between the distance of the zero from the origin and that of the pole from the origin.

## Slide 23: Design Procedure
Step-5
  Draw a new root-locus plot for the compensated system.
  Locate the desired dominant closed-loop poles on the root locus.
  (If the angle contribution of the lag network is very small—that is, a few degrees—then the original and new root loci are almost identical.
  Otherwise, there will be a slight discrepancy between them.
  Then locate, on the new root locus, the desired dominant closed-loop poles based on the transient-response specifications.

## Slide 24: Design Procedure
Step-6
  Adjust gain of the compensator from the magnitude condition so that the dominant closed-loop poles lie at the desired location.
  will be approximately 1.

## Slide 25: Example-1
Consider the system shown in following figure.
The damping ratio of the dominant closed-loop poles is . The undamped natural frequency of the dominant closed-loop poles is 0.673 rad/sec. The static velocity error constant is 0.53 sec–1.
It is desired to increase the static velocity error constant Kv to about 5 sec–1 without appreciably changing the location of the dominant closed-loop poles.

## Slide 26: Example-1 (Step-1)
The dominant closed-loop poles of given system are
s = -0.3307 ± j0.5864

## Slide 27: Example-1 (Step-2)
According to given conditions we need to add following compensator to fulfill the requirement.
=

## Slide 28: Example-1 (Step-3)
The static velocity error constant of the plant () is
The desired static velocity error constant () of the compensated system is .

## Slide 29: Example-1 (Step-3)

## Slide 30: Example-1 (Step-4)
Place the pole and zero of the lag compensator
Since , therefore
=
=

## Slide 31: Example-1 (Step-4)
Place the zero and pole of the lag compensator at s=–0.05 and s=–0.005, respectively.
The transfer function of the lag compensator becomes
Open loop transfer function is given as
=
Solution-1
=
=

## Slide 32: Example-1 (Step-5)
Root locus of uncompensated and compensated systems.
Solution-1
New Closed Loop poles are

## Slide 33: Example-1 (Step-5)
Root locus of uncompensated and compensated systems.
Solution-1

## Slide 34: Example-1 (Step-6)
The open-loop gain K is determined from the magnitude condition.
Then the compensator gain is determined as
Solution-1

## Slide 35: Example-1 (Step-6)
Then the compensator transfer function is given as
Solution-1

## Slide 36: Example-1 (Final Design Check)
The compensated system has following open loop transfer function.
Static velocity error constant is calculated as
Solution-1
=

## Slide 37: Example-1 (Step-4)
Place the zero and pole of the lag compensator at s=–0.01 and s=–0.001, respectively.
The transfer function of the lag compensator becomes
Open loop transfer function is given as
=
Solution-2
=
=

## Slide 38: Example-1 (Step-5)
Root locus of uncompensated and compensated systems.
Solution-2
New Closed Loop poles are

## Slide 39: Example-2
Design a lag compensator for following unity feedback system such that the static velocity error constant is 50 sec-1 without appreciably changing the closed loop poles, which are at.

## Slide 40: End of Lecture-8-9
To download this lecture visit
http://imtiazhussainkalwar.weebly.com/